## LABORATORY INSPECTION CHECKLIST

| Building & Room: |  | Inspected By: |  |
| --- | --- | --- | --- |
| PI/Area Supervisor: |  | Date: |  |

All laboratory spaces containing hazardous materials must be inspected at least quarterly. For each item check Yes, No, or N/A. Be sure to retain all documentation regarding inspections, including findings and corrective actions taken for any “No” responses, for a minimum of 3 years. Contact EH&S at 723-0448 for questions or additional information.

| Y | N | N/A | GENERAL SAFETY |
| --- | --- | --- | --- |
|  |  |  | Area around fire extinguishers, pull alarms, emergency showers, and electrical panels kept clear? |
|  |  |  | Eighteen-inch vertical clearance maintained below fire sprinkler heads (e.g., over shelves)? |
|  |  |  | Cabinets, furniture, and equipment taller than 4 feet braced or anchored? |
|  |  |  | Food and drink stored and consumed away from toxic and infectious materials? |
|  |  |  | Refrigerators/freezers labeled either “Food & Drink Only” or “No Food & Drink”? |
|  |  |  | Extension cords and power strips not daisy chained and no permanent extension cords in use? |
|  |  |  | No exposed wiring or damaged electrical cords? |
|  |  |  | Floors are clear and aisles and adjacent hallways unobstructed? |
|  |  |  | Floors dry and free of slip hazards; bench tops (including hoods) reasonably organized and clean? |
|  |  |  | HAZARDOUS MATERIALS & WASTES |
|  |  |  | All containers, including non-hazardous chemicals and wastes, legibly labeled with the full chemical or trade name (note: abbreviations/formulas are not adequate)? |
|  |  |  | All hazardous materials and oil pumps stored in secondary containment free of spilled material? |
|  |  |  | Incompatible materials properly segregated (see Stanford’s Storage Group Classification System)? |
|  |  |  | Chemical and waste containers in good condition and kept closed except during use (no funnels)? |
|  |  |  | Flammable liquids (including flammable waste and glacial acetic acid) stored in flammable liquid storage cabinets? Note: Up to 10 gallons per control area (NOT per individual lab) may be stored outside of cabinets. Control areas with cabinet credit are required to store 100% of their flammable liquid inventory inside cabinets. [CFC section 3404.3.4.1, 3404.3.4.4] |
|  |  |  | Flammables that are refrigerated are placed in explosion-proof or flammables refrigerators only? |
|  |  |  | No hazardous materials near sinks or drains unless secondary containment is provided? |
|  |  |  | Lab practices minimize volatilization (i.e. traps used, open-container procedures minimized)? |
|  |  |  | “Chemical Waste Compliance” poster posted in lab where hazardous waste is accumulated? |
|  |  |  | Storage in fume hoods minimized and sashes kept closed when not in use? |
|  |  |  | Emergency contacts, chemical storage maps, and chemical inventory in life safety box are current? |
|  |  |  | Hazardous material spill cleanup kits and first aid kits available (recommended)? |
|  |  |  | All hazardous wastes collected in compatible containers with completed waste tags and kept for no longer than 9 months from “accumulation date” on waste tag? |
|  |  |  | Biohazardous waste in red bags with proper signage in hard sided, closed secondary containment with biohazard symbols on four sides and top? |
|  |  |  | COMPRESSED GASES |
|  |  |  | Cylinders listed on chemical inventory, positioned so that contents label is visible, and stored in a dry, well-ventilated location protected from heat sources? |
|  |  |  | Cylinders > 26” tall secured to a rigid structure at 1/3 and 2/3 height with metal chains and a maximum of 2 cylinders per pair of chains (one restraint for cylinders <26” and dewars)? |
|  |  |  | Cylinder valves closed and valve caps in place when cylinders not in use? |

Comments & Additional Findings (on following page)

Comments & Additional Findings